## Slide 1: Subnetting 101

## Slide 2: Subnet by Class
Class 1st Octet # of Host Subnet Mask Broadcast
A 1 – 127 16,777,214 255.0.0.0 X.255.255.255
B 128 – 191 65,534 255.255.0.0 X.X.255.255
C 192 – 223 254 255.255.255.0 X.X.X.255
Where X means the value is held constant.

## Slide 3: Basic Formulas
Formulas
Number of Networks = 2x, x = bits borrow
Number of Hosts = 2y – 2, y = bits borrow

## Slide 4: Subnet Problem
Let take an example:
You are given a starting network address of 192.168.1.0./24, where /24 is 255.255.255.0
You are required to have at least 10 networks
Determine the following:
Number of Networks
Number of Hosts
Subnet Mask

## Slide 5: Solution
128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0 0 0 0 0
255. 255. 255 0
128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0
255 255 255 240 = 128+64+32+16
2x = 24 = 16 networks
2y – 2 = 24 – 2 = 16 – 2 = 14 hosts
Answer:
Number of Networks = 16
Number of Hosts = 14
Subnet Mask = 255.255.255.240

## Slide 6: Solution
128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0 0 0 0 0
255. 255. 255 0
128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0
255 255 255 240 = 128+64+32+16
2x = 24 = 16 networks
2y – 2 = 24 – 2 = 16 – 2 = 14 hosts
Answer:
Number of Networks = 16
Number of Hosts = 14
Subnet Mask = 255.255.255.240

## Slide 7: Subnet Problem
Let take an example:
You are given a starting network address of 172.16.1.0./24
You are required to have at least 50 hosts/network
Determine the following:
Number of Networks
Number of Hosts
Subnet Mask

## Slide 8: Solution
128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0 0 0 0 0
255. 255. 255 0
128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0 0 0
255 255 255 192 = 128+64
2x = 22 = 4 networks
2y – 2 = 26 – 2 = 64 – 2 = 62 hosts
Answer:
Number of Networks = 4
Number of Hosts = 62
Subnet Mask = 255.255.255.192

## Slide 9: Subnet Table
Network Address Host Range Broadcast Address
172.16.1.0 172.16.1.1 – 172.16.1.62 172.16.1.63
172.16.1.64 172.16.1.65 – 172.16.1.126 172.16.1.127
172.16.1.128 172.16.1.129 – 172.16.1.190 172.16.1.191
172.16.1.192 172.16.1.193 – 172.16.1.254 172.16.1.255